## Slide 1
Smart Waste Bin
Monitoring System
Using Fog & Edge Computing + AWS Cloud
SAPNA THAKUR | x24196614

## Slide 2
The Problem — Why Do We Need This?
X
Bins overflow
Collection trucks visit bins on a fixed schedule — Monday, Wednesday, Friday — no matter how full they are. Some bins overflow on Tuesday and sit there smelling bad for 2 days. Nobody knows until it is too late.
$
Wasted money & fuel
Trucks drive around collecting bins that are only 20% full. This wastes fuel, driver time and council money. Studies show up to 40% of collection trips are unnecessary because bins are not actually full yet.
?
No real-time data
There is no way to know which bins are full right now without physically driving to each one and looking inside. There is no data, no alerts, no system — just guessing based on a fixed schedule.
Our Solution:
Put 5 sensors on every bin → sensors send live data every few seconds → fog node processes it locally → AWS cloud stores it → dashboard shows which bins need collection RIGHT NOW

## Slide 3
How It Works — 3 Layers
Layer 1
Sensors
sensor_simulator.py
Runs on Mac
Fill level
Weight
Gas / Odour
Temperature
Lid status
Each sends data every 2-10 seconds
HTTP
POST
→
Layer 2
Fog Node
fog_node.py
Runs on Mac
Receives all sensor data
Validates every reading
Calculates avg / min / max
Saves data if cloud is down
Sends 1 summary to cloud every 10 seconds instead of 50 raw readings
Every
10s
→
Layer 3
AWS Cloud
cloud_backend.py
AWS Elastic Beanstalk
Receives fog data
Queue — handles spikes
3 workers — process data
Stores all readings
Serves REST API
Live 24/7 on AWS

## Slide 4
Dashboard — What the Examiner Sees
Anyone can open this link and see the live dashboard — no login, no setup, no local files needed:
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com
5 sensor cards
Shows latest value for fill level, weight, gas, temperature, lid — updates every 5 seconds automatically
4 live charts
Line charts showing how each sensor value has changed over time — you can see the bin slowly filling up
Alert system
Cards turn red with an ALERT badge when a sensor crosses its threshold — e.g. fill > 80% or gas > 400ppm
Bin selector
Dropdown to switch between different bins — BIN-001, BIN-002 etc. all shown separately
Alert feed
List of all recent alerts with timestamp, sensor name and value — full history of problem events
Auto refresh
Dashboard automatically pulls new data from AWS every 5 seconds — no manual refresh needed

## Slide 5
Live Demo — Open These Links Now
1
Live Dashboard
Open this first — show charts updating live with real sensor data
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com
2
Health Check — proof of scalability
Shows workers:3 (Lambda), queue_size (SQS), total_records going up
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com/api/health
3
API Documentation
FastAPI auto-generates this — shows all endpoints live on AWS
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com/docs
4
Live Sensor Data (JSON)
Real data stored on AWS — fill level, weight, gas, temp, lid
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com/api/latest/BIN-001
5
Alert Feed
Shows all alert events when sensors exceeded thresholds
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com/api/alerts/BIN-001
6
GitHub — Source Code
All 4 files with comments — full project code
https://github.com/thakursapna1996/smart-waste-bin

## Slide 6
What We Built & What We Learned
All requirements met
5 sensor types with configurable frequency
Virtual fog node — receives, validates, aggregates, dispatches
Scalable AWS backend — queue + 3 workers + auto-scaling
Live responsive dashboard on AWS — anyone can open it
Deployed and tested on AWS Elastic Beanstalk
Biggest challenge
AWS showed 502 Bad Gateway error after deployment
Problem: nginx expected port 5000 but app used 8080
Fix: switched to gunicorn on port 8000 with custom nginx config
Lesson: knowing the code is not enough — you must understand the full deployment stack too
http://Smart-waste-bin-env.eba-zvrsdqbr.us-east-1.elasticbeanstalk.com
THANK YOU